## Slide 1
VEK280 Vitis-AI
ML Deployment &
YOLOv7 Evaluation
AMD Versal AI Edge VEK280 (VE2802) · Vitis 2025.2 · Vitis-AI 6.2
Project technical summary

## Slide 2
The VEK280 board
Versal AI Edge VE2802 Adaptive SoC for embedded AI inference
VE2802 SoC: processing system, programmable logic and AI Engine-ML array
AIE-ML array: 38 columns × 8 rows (304 tiles)
12 GB LPDDR4 working memory
MicroSD boot, Ethernet, USB/JTAG, HDMI, FMC+, PCIe
Inference runs locally on the board, not the host

## Slide 3
Physical connections
Typical project setup
Power: supplied power input
Boot: MicroSD card
Host PC: Ethernet for SSH and file transfer
Console and debug: USB-UART / JTAG
Optional: USB webcam and HDMI display

## Slide 4
YOLOv7 architecture
One-stage, anchor-based detector with a fixed 640×640 input in this project
Input
640×640×3 RGB, letterbox resize, normalize
›
Backbone
Conv-BN-SiLU stem, E-ELAN blocks, MP downsampling → C3, C4, C5 features
›
Neck
SPPCSPC, then PAN/FPN top-down and bottom-up feature fusion
›
Head
RepConv per scale, 1×1 conv predicts box, objectness, class (3 anchors)
›
Post-process
Box decoding and NMS (conf 0.25, IoU 0.45)
Three detection scales
80×80 stride 8 · small objects
40×40 stride 16 · medium objects
20×20 stride 32 · large objects
Runs on the NPU (neural-network layers)
Runs on the Arm CPU (pre- and post-processing)

## Slide 5
From trained model to board
A .pt file is not run directly: the model is prepared for the NPU on the host
On the host (x86 Ubuntu)
On the board
1
Export
Trained YOLOv7 to ONNX
2
Quantize
INT8 for NPU execution
3
Compile
Map to VE2802_NPU_IP_O00_A304_M3
4
Snapshot
Deployable model built on x86 host
5
Deploy
Copy snapshot and app to MicroSD
6
Load
VART app loads snapshot, sends tensors
7
Infer
NPU runs network; CPU decodes and NMS
Deployed snapshot: /run/media/mmcblk0p1/snapshot.VE2802_NPU_IP_O00_A304_M3.yolov7.TF
Detector settings: fixed 640×640 input, confidence 0.25, NMS IoU 0.45

## Slide 6
Where the model runs on the board
Heavy neural-network math on the NPU; everything around it on the CPU
MicroSD
snapshot + app
USB webcam
or image file
Ethernet / HDMI
SSH, display
AMD Versal AI Edge VE2802
Processing system (Arm CPU)
Linux + VART runtime
Reads image or camera frame
Resize to 640×640, normalize
Box decoding and NMS
Draws and saves result
NPU (PL + AIE-ML)
INT8 YOLOv7 network layers
AIE-ML array: 38 × 8 = 304 tiles
PL datapath for control and data movement
About 63 ms per frame
input
output
12 GB LPDDR4: weights, activations and buffers

## Slide 7
YOLOv7 results
100-image baseline, 640×640 model input
63.1 ms
Mean NPU latency
15.8 FPS
NPU throughput
0.315 FPS
End-to-end throughput
≈3.3 W
Monitored rail power (INA226)
NPU latency stayed about the same from 320×240 to 1920×1080 sources, because the model input is fixed at 640×640
Live webcam: about 14.2 NPU FPS but 0.31 end-to-end FPS
The bottleneck is the surrounding pipeline (pre/post-processing, I/O), not the NPU
Energy is about 10.5 J per image; power is a rail measurement, not total board power