## Slide 1
YOLOv7 Deployment and NPU-Only Performance Evaluation on the AMD Versal AI Edge VEK280
Final evaluation: NPU-only mode, CPU subgraphs disabled / skipped
Board | AMD Versal AI Edge VEK280 / VE2802 | Vitis / Vitis-AI | 2025.2 / 6.2
Model | YOLOv7, fixed 640 × 640 | NPU | VE2802 NPU, A304 configuration
Execution | NPU-only, CPU subgraphs skipped | Runner | Native VART/NPU runner

## Slide 2
VEK280 hardware and connections
VE2802 SoC: processing system, programmable logic and AIE-ML array (304 tiles, NPU at 500 MHz)
12 GB LPDDR4; MicroSD boot; Ethernet, USB-UART, HDMI and USB webcam
Powered from its supplied input, boots from MicroSD, Ethernet to host for SSH and file transfer, USB-UART for console

## Slide 3
NPU architecture and deployment flow
Where each stage executes
Stage | Executes on
Read/decode, letterbox, input preparation | CPU (processing system)
INT8 neural-network inference | NPU (PL + AIE-ML)
Output decode, NMS, drawing | CPU (processing system)
Model data and buffers | LPDDR4
The VEK280 uses the AI Engine-based NPU, not the DPU of earlier platforms, so the model is compiled specifically for the VE2802 NPU. Compilation is not pruning.
Deployment flow
Host: export model to ONNX
Host: INT8 quantization
Host: compile for VE2802 NPU (A304)
Host: package the snapshot
Board: copy snapshot to MicroSD
Board: VART app loads it and feeds tensors
Board: decode and NMS on NPU output
Snapshot: /run/media/mmcblk0p1/snapshot.VE2802_NPU_IP_O00_A304_M3.yolov7.TF

## Slide 4
YOLOv7 final configuration: NPU-only
Parameter | Value
Application input | (1, 3, 640, 640) float32 NCHW
Native NPU input | (1, 640, 640, 4) INT8 NHWC4
Output tensor | (1, 25200, 85)
Confidence / NMS IoU | 0.25 / 0.45
CPU subgraph is skipped; the network runs fully on the NPU
Gives a clean accelerator measurement and one consistent configuration
CPU still handles image handling, decode, NMS and display
NPU only mode set. Skipping node wrp_network_embd_export_2_cpu_subgraph_call.

## Slide 5
Final NPU-only profiling results
ms per frame | 320×240 | 640×480 | 1280×720 | 1920×1080
Read/decode | 9.52 | 16.07 | 30.50 | 44.31
Letterbox | 4.58 | 0.69 | 3.17 | 7.97
Preparation | 12.78 | 12.41 | 12.25 | 12.22
NPU | 7.18 | 7.14 | 7.12 | 7.12
Decode+NMS+Draw | 2.94 | 3.24 | 3.25 | 3.35
Frame total | 37.02 | 39.57 | 56.32 | 74.99
End-to-end FPS | 27.01 | 25.27 | 17.76 | 13.33
CPU busy | 72% | 72% | 80% | 95%
101 images at each of four source resolutions (404/404 completed). Values are per-frame averages from the stage-level profiler. Model input is fixed at 640×640.

## Slide 6
Analysis
NPU latency is stable at 7.12–7.18 ms (ceiling about 140 FPS), about 10× the best end-to-end rate
Read/decode rises 4.7× (9.52 to 44.31 ms) and is about 59% of frame time at 1920×1080; CPU load reaches 95%
Input preparation is a fixed 12.2–12.8 ms cost, larger than the NPU stage; decode, NMS and drawing add only about 3 ms
VART runner: 175.44 ms with CPU subgraph (development baseline) fell to 73.75 ms NPU-only, 2.38× faster
Next: faster decode and resize, overlapped with NPU execution

## Slide 7
AIE-ML activity, power and conclusions
Metric | Value
AIE-ML activity, 320×240 to 1280×720 | 51.65–52.07%
AIE-ML activity, 1920×1080 | 61.45% (tiles 59.19–64.40%)
AIE-ML activity, later 1920×1080 run | 52.48% (52.21–52.77%)
Average power (4 resolutions) | 3.546–3.565 W
Peak power | 3.705–3.966 W
Energy per frame | 0.131–0.267 J
AIE profiling adds large overhead (1920×1080: 74.99 ms rose to about 136 ms), so it is never used for benchmarks. Power is the INA226 monitored rail, not total board power.
Conclusions
YOLOv7 runs on the VE2802 NPU, evaluated in NPU-only mode with CPU subgraphs disabled/skipped
NPU inference is a stable 7.1 ms; the full pipeline reaches 13.33–27.01 FPS
Throughput is limited by CPU-side decode and preparation, not the NPU
ResNet50 and YOLOX-S were also deployed; video and webcam demos use the same NPU-only pipeline